## Slide 1: Comparative Analysis of Traditional and Modern Memory Translation Architectures
OPERATING SYSTEMS COURSE PROJECT (B2 + TB2)
Which page table is best, what real operating systems use and why, and what they would gain or lose by switching.
Akhilesh Regmi 24BCE2934
Swayam Raj Pandey 24BCE2933
Aamarsh Raj Shakya 24BDS0449
UNDER THE GUIDANCE OF
Prof. Manivannan P
All latencies are modelled cycles from a stated cost model, not hardware measurements.
Notes: Three parts: a simulator comparing four page-table organizations, a study of what real operating systems use, and a what-if analysis of switching. Every latency comes from our cost model, not measured hardware.

## Slide 2: Introduction: what this project is
Every memory access needs its virtual address translated. When the TLB misses, the page table is walked in memory: 4 reads on x86-64, up to 24 when virtualized. How the table is organized sets that cost. We asked three questions:
1
Comparison
Which of four page-table organizations performs best, and when?
2
OS study
What do Windows, Linux, macOS and Android use, and why?
3
What if
What would each OS gain or lose by switching technique?
WHAT WE HAVE DONE
4
page tables built and walked for real, behind one shared TLB
5
parameter sweeps, one graph each
6
OS platforms studied from documentation
60
what-if runs across those platforms
65
automated tests, plus an interactive app
Notes: What the project is: every memory access needs a translation, and a TLB miss walks the page table: 4 reads on x86-64, 24 when virtualized. We built a simulator to compare page-table organizations, then used it to study real operating systems. What we have done is in the bottom row.

## Slide 3: Four ways to organize a page table
PART 1 · COMPARISON
Single-level
One flat array per process, indexed by page number.
+ 1 read per miss
– Size covers the whole address span
Multi-level (radix)
A tree; only the branches in use exist.
+ Tiny for sparse address spaces
– 1 read per level: 4 on x86-64
Hashed
Hash of (process, page) selects a chain.
+ About 1 read per miss
– Scatters entries; huge pages are hard
Inverted
One entry per physical frame, shared by all.
+ Size follows RAM only
– Anchor read plus chain; sharing is awkward
Notes: The four organizations. Each colour is that organization's colour in every chart that follows.

## Slide 4: Method: one trace, one TLB, four real walks
PART 1 · COMPARISON
1
Workload
Seeded trace of 100,000 accesses; sequential, strided, random or Zipf-skewed; 16 MiB per process.
2
TLB
One shared LRU TLB, flushed on context switch. Hits are identical for every table.
3
Walk
Each miss walks a real data structure and counts its memory reads.
4
Cost
1 cycle per access + 100 per memory read + 10 per hash on a miss.
BASELINE
4 KB pages · 64-entry TLB · 16 GiB address span, 4 GiB RAM · skewed access · 1 process
Sweeps: page size 4 KB–2 MB · TLB off–1024 entries · memory small/medium/large · four patterns · 1–16 processes
Notes: Every organization replays exactly the same trace, so differences come only from the table. One factor changes at a time from the baseline.

## Slide 5: Baseline: the fastest table is not the smallest
PART 1 · COMPARISON
Organization | Latency (cycles) | Reads / access | Table memory
single-level | 62.0 | 0.61 | 32 MiB
hashed | 68.3 | 0.61 | 4.1 MiB
inverted | 129.5 | 1.22 | 20 MiB
multi-level | 245.2 | 2.44 | 60 KiB
TLB hit rate is 0.39 for all four: it depends on the trace and the TLB, not on the table.
546x
the table memory for single-level versus multi-level
4x
the memory reads for multi-level: the price of being small
Notes: Single-level is fastest, multi-level smallest. Hashed gets within about 10% of single-level latency with an eighth of its memory.

## Slide 6: Page size and locality drive latency
PART 1 · COMPARISON
Chart: (a) Latency vs page size
| 4 KB | 16 KB | 64 KB | 2 MB
single-level | 62.046 | 59.269 | 45.892 | 1.008
multi-level | 245.184 | 234.076 | 135.676 | 1.024
hashed | 68.2566 | 65.0959 | 50.9102 | 1.0088
inverted | 129.4576 | 123.3649 | 95.7442 | 1.0168
Chart: (d) Latency by access pattern
| sequential | strided | random | skewed
single-level | 2.563 | 101 | 99.403 | 62.046
multi-level | 7.252 | 401 | 394.612 | 245.184
hashed | 2.7193 | 111.318 | 109.5813 | 68.2566
inverted | 4.2923 | 211.321 | 207.9663 | 129.4576
Multi-level: 245.2 cycles at 4 KB, 135.7 at 64 KB, about 1 at 2 MB.
Sequential access costs under 8 cycles for every table; strided costs multi-level 401.0.
Notes: Graphs a and d. Bigger pages widen TLB reach; at 2 MB the 16 MiB working set fits in 8 entries. The access pattern moves latency by two orders of magnitude.

## Slide 7: The TLB sets how often you miss; the table sets the price
PART 1 · COMPARISON
Chart: (b) TLB hit rate vs TLB size (same for all four tables)
| off | 16 | 64 | 256 | 1024
all four organizations | 0 | 0.21109 | 0.38954 | 0.57669 | 0.77588
Chart: (e) Latency vs number of processes
| 1 | 2 | 4 | 8 | 16
single-level | 62.046 | 62.872 | 62.988 | 62.792 | 62.958
multi-level | 245.184 | 248.488 | 248.952 | 248.168 | 248.832
hashed | 68.2566 | 69.3692 | 70.1908 | 71.2922 | 72.9688
inverted | 129.4576 | 131.5252 | 132.3718 | 132.5752 | 135.2318
All four lines coincide: hit rate goes from 0 to 0.78 whatever the table.
Hashed rises 68.3 to 73.0 cycles as one shared table fills up; per-process tables stay flat.
Notes: Graph b: the hit-rate lines coincide by construction. Graph e: global tables (hashed, inverted) get longer chains as processes are added; per-process tables stay flat.

## Slide 8: Each table's size follows something different
PART 1 · COMPARISON
Chart: (c) Page-table memory vs memory size
| small | medium | large
single-level | 2 | 32 | 512
multi-level | 0.042969 | 0.058594 | 0.070312
hashed | 0.59375 | 4.0938 | 16.0938
inverted | 2.5 | 20 | 80
Single-level
follows the address span: 2.0 MiB → 512 MiB
Inverted
follows physical memory: 2.5 MiB → 80 MiB
Hashed
follows its bucket array: 608 KiB → 16 MiB
Multi-level
follows only what is mapped: under 72 KiB
Notes: Graph c, log scale. Small, medium and large are 1, 16 and 256 GiB of address span with 0.5, 4 and 16 GiB of RAM: our choice.

## Slide 9: The hardware decides the table; the OS decides the page size
PART 2 · OS STUDY
Operating system | CPU | Page table (set by the CPU) | Page size (set by the OS)
Windows x64 | x86-64 | multi-level, 4 levels | 4 KB; 2 MB large pages on request
Linux x86-64 | x86-64 | multi-level, 4 or 5 levels | 4 KB; transparent 2 MB huge pages
macOS, Apple Silicon | Arm | multi-level | 16 KB
Android | Arm | multi-level | 4 KB, 16 KB from Android 15
Linux ARM64 servers | Arm | multi-level | 4 KB or 64 KB, chosen at build
Linux on IBM POWER9 | POWER | radix by default, or hashed | 64 KB
Every mainstream OS uses a multi-level table because the CPU walks it in hardware. Only POWER9 lets the OS choose another organization.
Notes: Central finding of the OS study. On x86-64 and Arm the MMU walks a radix tree in hardware, so every OS uses it. What each OS really chooses is the page size. POWER9 is the exception.

## Slide 10: Why each OS chose its page size
PART 2 · OS STUDY
OS | Why | Upside | Downside
Windows x64 | Fine-grained memory for many desktop processes | Low waste; pages swap individually | Little TLB reach; large pages need privilege and contiguous RAM
Linux x86-64 | Low waste by default, reach where it pays | Huge pages with no app changes (THP) | THP can cause latency spikes and memory bloat
macOS | Apple controls chip and OS together | 4x the TLB reach of 4 KB | More rounding waste; 4 KB-era software had to adapt
Android | App ecosystem was built on 4 KB | 16 KB: launch 3.2% and boot 8% faster | 16 KB: slightly more memory; libraries rebuilt
Linux ARM64 | Arm offers 4, 16 and 64 KB granules | 64 KB: fewer levels, 16x reach | Up to 64 KB waste per allocation; fixed per build
Sources: Microsoft Learn, Linux kernel docs, Apple WWDC20, Android Developers (16 KB page sizes). Full list in the report.
Notes: Each OS's page-size choice, why, and what it gains and loses. Android's numbers are Google's own measurements.

## Slide 11: POWER9: the one platform where the OS can switch
PART 2 · OS STUDY
Hashed page table
Traditional on POWER; still available at boot (disable_radix)
About two cache-line reads per translation
Entries scatter, so most misses go to main memory
Radix tree (default)
Added in Power ISA 3.0; hardware walks Linux's own tables
Neighbouring entries share cache lines
Linux default, with 64 KB pages
Our model, 64 KB pages | Radix latency | Hashed latency | Radix memory | Hashed memory
1 process | 135.7 | 50.9 | 512 KiB | 262 KiB
16 processes | 142.9 | 56.0 | 9.1 MiB | 352 KiB
IBM: radix “is expected to be more efficient than HPT translation for workloads with high locality of references.”
Notes: IBM moved Linux on POWER from a hashed table to a radix tree. Our model favours hashed, but IBM chose radix for cache behaviour our model does not capture.

## Slide 12: Switching organization: faster in the model, but not possible
PART 3 · WHAT IF
Option | Latency | Change | Memory, 1 process | Memory, 16 processes
Today: multi-level | 245.2 | – | 60 KiB | 1.0 MiB
Switch to single-level | 62.0 | -75% | 32 MiB | 512 MiB
Switch to hashed | 68.3 | -72% | 4.1 MiB | 5.5 MiB
Switch to inverted | 129.5 | -47% | 20 MiB | 20 MiB
Windows x64, Linux x86-64, Linux ARM64 and Android (all 4 KB multi-level) give identical results.
Gain
Up to 75% lower modelled latency: multi-level pays 4 reads per miss.
Loss
70x the table memory for hashed; single-level reaches 512 MiB at 16 processes.
Feasible?
No. The x86-64 and Arm MMUs walk only radix tables; this needs new hardware.
Notes: Each OS re-run with the other three organizations. Shown for the 4 KB x86-64 and Arm systems, which give identical results. Lower latency, far more memory, and the CPU would not walk it.

## Slide 13: Switching page size: the switch an OS can really make
PART 3 · WHAT IF
OS | Switch | Latency | Table memory | Worst-case waste, 1000 allocations
Windows x64 | 4 KB → 2 MB | -99.6% | 60 KiB → 28 KiB | 3.9 MiB → 2000 MiB
Linux x86-64 | 4 KB → 2 MB | -99.6% | 60 KiB → 28 KiB | 3.9 MiB → 2000 MiB
macOS | 16 KB → 4 KB | +5% | 176 KiB → 60 KiB | 16 MiB → 3.9 MiB
Android | 4 KB → 16 KB | -5% | 60 KiB → 176 KiB | 3.9 MiB → 16 MiB
Linux ARM64 | 4 KB → 64 KB | -45% | 60 KiB → 512 KiB | 3.9 MiB → 62 MiB
Linux POWER9 | 64 KB → 4 KB | +81% | 512 KiB → 60 KiB | 62 MiB → 3.9 MiB
Android's 16 KB move matches Google's measurements: faster launches and boot, slightly more memory. 2 MB pages stay opt-in because they can waste up to 2 MB per allocation.
Notes: Each OS re-run at its alternative page size. Larger pages buy latency with rounding waste; smaller pages do the reverse.

## Slide 14: Model versus reality: our gains are upper bounds
PART 3 · WHAT IF
72%
lower latency for x86-64 switching to a hashed table, in our model
1–27%
shorter runtimes measured for an optimized hashed table on real x86-64 (Yaniv and Tsafrir, 2016)
Real CPUs have page-walk caches: most misses cost one or two reads, not four.
Our model has no caches and charges every read the full 100 cycles, so it overstates the radix penalty.
Same direction, smaller size: treat the what-if latency gains as upper bounds; the memory costs hold.
Notes: Real CPUs cache the upper radix levels, so most misses cost one or two reads, not four. Our model charges every read the full 100 cycles. Direction agrees, size does not.

## Slide 15
CONCLUSIONS
Every table trades memory for reads, and the CPU picks the table
Comparison: single-level is fastest but huge; multi-level is tiny but reads every level; hashed is the best balance.
OS study: Windows, Linux, macOS and Android all use the radix tree their CPU walks; their real choice is page size.
What if: other organizations cut modelled latency but multiply memory, and need new hardware outside POWER.
Page size is the lever an OS really has; Android's move to 16 KB is that trade-off in practice.
LIMITS AND NEXT STEPS
Modelled latency, synthetic traces, no page-walk caches. Next: add a page-walk cache, implement ECPT or FPT from Review 1, replay real traces.
Notes: One conclusion per part of the project, then the limits of the model and what we would do next. The interactive simulator (streamlit run app.py) has OS study and What-if tabs.